| Tank In-service Inspection Checklist |
| --- |
| Item | Completed √ | Comments |
| C.1.1 Foundation |  |  |
| Measure foundation levelness and bottom elevations (see Annex B for extent of measurements). | √ | See 4.6 |
| C.1.1.1 Concrete Ring |  |  |
| a) Inspect for broken concrete, spalling, and cracks, particularly under backup bars used in welding butt-welded annular rings under the shell. | √ | See 4.4.3 |
| b) Inspect drain openings in ring, back of waterdraw basins and top surface of ring for indications of bottom leakage. | √ |  |
| c) Inspect for cavities under foundation and vegetation against bottom of tank. | √ | See 4.4.3 |
| d) Check that runoff rainwater from the shell drains away from tank. | √ |  |
| e) Check for settlement around perimeter of tank. | √ | See 4.6 |
| C.1.1.2 Asphalt |  |  |
| a) Check for settling of tank into asphalt base which would direct runoff rain water under the tank instead of away from it. | n/a |  |
| b) Look for areas where leaching of oil has left rock filler exposed, which indicates hydrocarbon leakage. | n/a |  |
| C.1.1.3 Oiled Dirt or Sand |  |  |
| Check for settlement into the base which would direct runoff rain water under the tank rather than away from it. | n/a |  |
| C.1.1.4 Rock |  |  |
| Presence of crushed rock under the steel bottom usually results in severe underside corrosion. Make a note to do additional bottom plate examination (ultrasonic, hammer testing, or turning of coupons) when the tank is out of service. | n/a |  |
| C.1.1.5 Site Drainage |  |  |
| a) Check site for drainage away from the tank and associated piping and manifolds. | √ |  |
| b) Check operating condition of the dike drains. | √ |  |
| C.1.1.6 Housekeeping |  |  |
| Inspect the area for buildup of trash, vegetation, and other inflammables buildup. | √ |  |
| C.1.1.7 Cathodic Protection |  |  |
| Review cathodic protection potential readings. | n/a |  |
| C.1.2 Shells |  |  |
| C.1.2.1 External Visual Inspection |  |  |
| a) Visually inspect for paint failures, pitting, and corrosion. | √ | See 4.1 |
| b) Clean off the bottom angle area and inspect for corrosion and thinning on plate and weld. | √ | See 4.4.3 |
| c) Inspect the bottom-to-foundation seal, if any. | n/a | See 4.4.3 |
| C.1.2.2 Internal (Floating Roof Tank) |  |  |
| Visually inspect for grooving, corrosion, pitting, and coating failures. | n/a |  |
| C.1.2.3 Riveted Shell Inspection |  |  |
| a) Inspect external surface for rivet and seam leaks. | n/a |  |
| b) Locate leaks by sketch or photo (location will be lost when shell is abrasive cleaned for painting). | n/a |  |
| c) Inspect rivets for corrosion loss and wear. | n/a |  |
| d) Inspect vertical seams to see if they have been full fillet lap-welded to increase joint efficiency. | n/a |  |
| e) If no record exists of vertical riveted seams, dimension and sketch (or photograph) the rivet pattern: number of rows, rivet size, pitch length, and note whether the joint is butt-riveted or lap-riveted. | n/a |  |
| C.1.2.4 Wind Girder (Floating Roof Tanks) |  |  |
| a) Inspect wind girder and handrail for corrosion damage (paint failure, pitting, corrosion product buildup), especially where it occurs at tack-welded junction, and for broken welds. | n/a |  |
| b) Check support welds to shell for pitting, especially on shell plates. | n/a |  |
| c) Note whether supports have reinforcing pads welded to shell. | n/a |  |
| C.1.3 Shell Appurtenances |  |  |
| C.1.3.1 Manways and Nozzles |  |  |
| a) Inspect for cracks or signs of leakage on weld joint at nozzles, manways, and reinforcing plates. | √ | See 4.1 |
| b) Inspect for shell plate dimpling around nozzles, caused by excessive pipe deflection. | √ | See 4.1 |
| c) Inspect for flange leaks and leaks around bolting. | n/a | Tank is out-of-service |
| d) Inspect sealing of insulation around manways and nozzles. | n/a | No insulation |
| e) Check for inadequate manway flange and cover thickness on mixer manways. | √ | See 4.1 and tables 4.3, 4.4 and 4.5 |
| C.1.3.2 Tank Piping Manifolds |  |  |
| a) Inspect manifold piping, flanges, and valves for leaks. | n/a | Tank is out-of-service |
| b) Inspect fire fighting system components. | n/a | There is none |
| c) Check for anchored piping which would be hazardous to the tank shell or bottom connections during earth movement. | n/a |  |
| d) Check for adequate thermal pressure relief of piping to the tank. | n/a |  |
| e) Check operation of regulators for tanks with purge gas systems. | n/a |  |
| f) Check sample connections for leaks and for proper valve operation. | n/a | No sample connections |
| g) Check for damage and test the accuracy of temperature indicators. | n/a | Not included in the inspection |
| h) Check welds on shell-mounted davit clips above valves 6 in. and larger. | n/a | There is none |
| C.1.3.3 Autogauge System |  |  |
| a) Inspect autogauge tape guide and lower sheave housing (floating swings) for leaks. | n/a |  |
| b) Inspect autogauge head for damage. | n/a |  |
| c) Bump the checker on autogauge head for proper movement of tape. | n/a |  |
| d) Identify size and construction material of autogauge tape guide (floating roof tanks). | n/a |  |
| e) Ask operator if tape tends to hang up during tank roof movement (floating roof tanks). | n/a |  |
| f) Compare actual product level to the reading on the autogauge (maximum variation is 2 in.). | n/a |  |
| Item | Completed √ | Comments |
| g) On floating roof tanks, when the roof is in the lowest position, check that no more than two ft of tape are exposed at the end of the tape guide. | n/a |  |
| h) Inspect condition of board and legibility of board-type autogauges. | n/a |  |
| i) Test freedom of movement of marker and float. | n/a |  |
| C.1.3.4 Shell-mounted Sample Station |  |  |
| a) Inspect sample lines for function of valves and plugging of lines, including drain or return-to-tank line. | n/a | There is no sample station |
| b) Check circulation pump for leaks and operating problems. | n/a |  |
| c) Test bracing and supports for sample lines and equipment. | n/a |  |
| C.1.3.5 Heater (Shell Manway Mounted) |  |  |
| Inspect condensate drain for presence of oil indicating leakage. | n/a |  |
| C.1.3.6 Mixer |  |  |
| a) Inspect for proper mounting flange and support. | n/a |  |
| b) Inspect for leakage. | n/a |  |
| c) Inspect condition of power lines and connections to mixer. | n/a |  |
| C.1.3.7 Swing Lines: Winch Operation |  |  |
| a) Nonfloating. Raise, then lower the swing line with the winch, and check for cable tightness to confirm that swing line lowered properly. | n/a |  |
| b) Floating. With tank half full or more, lower the swing line, then let out cable and check if swing has pulled cable tight, indicating that the winch is operating properly. | n/a |  |
| c) Indicator. Check that the indicator moves in the proper direction: Floating swing line indicators show a lower level as cable is wound up on the winch. Non-floating swing line indicators show the opposite. | n/a |  |
| C.1.3.8 Swing Lines: External Guide System |  |  |
| Check for leaks at threaded and flanged joints. | n/a |  |
| C.1.3.9 Swing Lines: Identify Ballast Varying Need |  |  |
| Check for significant difference in stock specific gravity. | n/a |  |
| C.1.3.10 Swing Lines: Cable Material and Condition |  |  |
| a) For nonstainless steel cable, check for corrosion over entire length. | n/a |  |
| b) All cable: check for wear or fraying. | n/a |  |
| C.1.3.11 Swing Lines: Product Sample Comparison |  |  |
| Check for water or gravity differences that would indicate a leaking swing joint. | n/a |  |
| C.1.3.12 Swing Lines: Target |  |  |
| Target should indicate direction of swing opening (up or down) and height above bottom where suction will be lost with swing on bottom support. | n/a |  |
| C.1.4 Roofs |  |  |
| C.1.4.1 Deck Plate Internal Corrosion |  |  |
| For safety, before accessing the roof, check with ultrasonic instrument or lightly use a ball peen hammer to test the deck plate near the edge of the roof for thinning. (Corrosion normally attacks the deck plate at the edge of a fixed roof and at the rafters in the center of the roof first.) | √ | See table 4.12 |
| C.1.4.2 Deck Plate External Corrosion |  |  |
| Visually inspect for paint failure, holes, pitting, and corrosion product on the roof deck. | √ | See 4.3.1. for recommendation |
| C.1.4.3 Roof Deck Drainage |  |  |
| Look for indication of standing water. (Significant sagging of fixed roof deck indicates potential rafter failure. Large standing water areas on a floating roof indicate inadequate drainage design or, if to one side, a nonlevel roof with possible leaking pontoons.) | √ |  |
| C.1.4.4 Level of Floating Roof |  |  |
| At several locations, measure distance from roof rim to a horizontal weld seam above the roof. A variance in the readings indicates a nonlevel roof with possible shell out-of-round, out-of-plumb, leaking pontoons, or hang-up. On small diameter tanks, an unlevel condition can indicate unequal loading at that level. | n/a |  |
| C.1.4.5 Gas Test Internal Floating Roof |  |  |
| Test for explosive gas on top of the internal floating roof. Readings could indicate a leaking roof, leaking seal system, or inadequate ventilation of the area above the internal floating roof. | n/a |  |
| C.1.4.6 Roof Insulation |  |  |
| a) Visually inspect for cracks or leaks in the insulation weather coat where runoff rain water could penetrate the insulation. | n/a |  |
| b) Inspect for wet insulation under the weather coat. | n/a |  |
| c) Remove small test sections of insulation and check roof plate for corrosion and holes near areas susceptible to water ingress (i.e. roof nozzles, etc.). | n/a |  |
| C.1.4.7 Floating Roof Seal Systems |  |  |
| a) Inspect the condition of the seal, measure and record maximum rim spaces and seal- to-shell gaps around the full roof circumference at the level of inspection. NOTE Inspection of the seal and measurement of the rim spaces and seal-to-shell gaps at more than one level may be necessary to more fully determine if any problems exist at other levels of tank operation). | n/a |  |
| b) Measure and record annular space at 30-ft spacing (minimum of four quadrants) around roof and record. Measurements should be taken in directly opposite pairs. | n/a |  |
| 1) Opposite pair 1. 2) Opposite pair 2. | n/a |  |
| c) Check if seal fabric on primary shoe seals is pulling shoes away from shell (fabric not wide enough). | n/a |  |
| d) Inspect fabric for deterioration, holes, tears, and cracks. | n/a |  |
| e) Inspect visible metallic parts for corrosion and wear. | n/a |  |
| f) Inspect for openings in seals that would permit vapor emissions. | n/a |  |
| g) Inspect for protruding bolt or rivet heads against the shell. | n/a |  |
| h) Pull both primary and secondary seal systems back all around the shell to check their operation. | n/a |  |
| i) Inspect secondary seals for signs of buckling or indications that their angle with the shell is too shallow. | n/a |  |
| j) Inspect wedge-type wiper seals for flexibility, resilience, cracks, and tears. | n/a |  |
| C.1.5 Roof Appurtenances |  |  |
| C.1.5.1 Sample Hatch |  |  |
| a) Inspect condition and functioning of sample hatch cover. | n/a |  |
| b) On tanks governed by Air Quality Monitoring District rules, check for the condition of seal inside hatch cover. | n/a |  |
| c) Check for corrosion and plugging on thief and gauge hatch cover. | n/a |  |
| d) Where sample hatch is used to reel gauge stock level, check for marker and tab stating hold-off distance. | n/a |  |
| e) Check for reinforcing pad where sample hatch pipe penetrates the roof deck. | n/a |  |
| f) On floating roof sample hatch and recoil systems, inspect operation of recoil reel and condition of rope. | n/a |  |
| g) Test operation of system. | n/a |  |
| h) On ultra clean stocks such as JP4, check for presence and condition of protective coating or liner inside sample hatch (preventing rust from pipe getting into sample). | n/a |  |
| C.1.5.2 Gauge Well |  |  |
| a) Inspect visible portion of the gauge well for thinning, size of slots, and cover condition. | √ |  |
| b) Check for a hold-off distance marker and tab with hold-off distance (legible). | n/a |  |
| c) On floating roofs, inspect condition of roof guide for gauge well, particularly the condition of the rollers for grooving. | n/a |  |
| d) If accessible, check the distance from the gauge well pipe to the tank shell at different levels. | n/a | Not accesible |
| e) If tank has a gauge well washer, check valve for leakage and for presence of a bull plug or blind flange. | n/a | Not present |
| C.1.5.3 Fixed Roof Scaffold Support |  |  |
| Inspect scaffold support for corrosion, wear, and structural soundness. | n/a |  |
| C.1.5.4 Autogauge: Inspection Hatch and Guides (Fixed Roof) |  |  |
| a) Check the hatch for corrosion and missing bolts. | n/a |  |
| b) Look for corrosion on the tape guide’s and float guide’s wire anchors. | n/a |  |
| C.1.5.5 Autogauge: Float Well Cover |  |  |
| a) Inspect for corrosion. | n/a |  |
| b) Check tape cable for wear or fraying caused by rubbing on the cover. | n/a |  |
| C.1.5.6 Sample Hatch (Internal Floating Roof) |  |  |
| a) Check overall conditions. | n/a |  |
| b) When equipped with a fabric seal, check for automatic sealing after sampling. | n/a |  |
| c) When equipped with a recoil reel opening device, check for proper operations. | n/a |  |
| C.1.5.7 Roof-mounted Vents (Internal Floating Roof) |  |  |
| Check condition of screens, locking and pivot pins. | n/a |  |
| C.1.5.8 Gauging Platform Drip Ring |  |  |
| On fixed roof tanks with drip rings under the gauging platform or sampling area, inspect for plugged drain return to the tank. | n/a |  |
| C.1.5.9 Emergency Roof Drains |  |  |
| Inspect vapor plugs for emergency drain: that seal fabric discs are slightly smaller than the pipe ID and that fabric seal is above the liquid level. | n/a |  |
| C.1.5.10 Removable Roof Leg Racks |  |  |
| Check for leg racks on roof. | n/a |  |
| C.1.5.11 Vacuum Breakers |  |  |
| Report size, number, and type of vacuum breakers. Inspect vacuum breakers. If high legs are set, check for setting of mechanical breaker in high leg position. | n/a |  |
| C.1.5.12 Rim Vents |  |  |
| a) Check condition of the screen on the rim vent cover. | n/a |  |
| b) Check for plating off or removal of rim vents where jurisdictional rules do not permit removal. | n/a |  |
| C.1.5.13 Pontoon Inspection Hatches |  |  |
| a) Open pontoon inspection hatch covers and visually check inside for pontoon leakage. | n/a |  |
| b) Test for explosive gas (an indicator of vapor space leaks). | n/a |  |
| c) If pontoon hatches are equipped with locked down coves, check for vent tubes. Check that vent tubes are not plugged up. Inspect lock-down devices for condition and operation. | n/a |  |
| C.1.6 Accessways |  |  |
| See Tank Out-of-service Inspection Checklist, Item C.2.12. | n/a |  |